## Slide 1
We feed the machine the following program:
loop:
flw f1, -4(t0)
fmul.s f2, f1, f0
fsw f2, -4(t0)
addi t0, t0, -4
bnez t0, loop
fmul.s f3,f2,f4 #just filling
fsub.s f5,f1,f2
fdiv.s f0,f3,f1
fadd.s f1,f5,f2
loads and stores take 2 cycles
float muls/divs take 4 cycles
float adds/subs take 3 cycles
integer operations take 2 cycles
The branch predictor is correct at the first bnez instruction and takes the loop.
The second time it finds the bnez, it predicts jump and is wrong, the ROB needs to be flushed.
The loop performs a float vector multiplication by a scalar in F0

## Slide 2
Cycle 0
Inst. Queue.
Reorder Buffer
Registers
Load Buffer
Reservation Station (FP)
Reservation Station (Int)
Common Data Bus
flw f1, -4(t0)
bnez t0, loop
addi t0, t0, -4
fsw f2, -4(t0)
fmul.s f2, f1, f0
flw f1, -4(t0)
0 |  |  | 
1 |  |  | 
2 |  |  | 
3 |  |  | 
4 |  |  | 
5 |  |  | 
F0 | 10 | 
F1 | 0 | ROB0
F2 | 0 | 
T0 | 8 | 
FP ALU
Int ALU
Memory Unit
stores
loads
inst.
commit
Op.+ROB#
operands
results

## Slide 3
Cycle 1
The first load is sent through the pipeline to the Load buffer and the ROB.
Inst. Queue.
Reorder Buffer
Registers
Load Buffer
Reservation Station (FP)
Reservation Station (Int)
Common Data Bus
4 | ROB0
fmul.s f2, f1, f0
flw f1, -4(t0)
bnez t0, loop
addi t0, t0, -4
fsw f2, -4(t0)
fmul.s f2, f1, f0
0 | FLW | F1 | 
1 |  |  | 
2 |  |  | 
3 |  |  | 
4 |  |  | 
5 |  |  | 
F0 | 10 | 
F1 | 0 | ROB0
F2 | 0 | 
T0 | 8 | 
FP ALU
Int ALU
Memory Unit
loads
inst.
commit
Op.+ROB#
operands
results
stores
flw f1, -4(t0)
flw f1, -4(t0)

## Slide 4
Cycle 2
The first load is sent to the Memory Unit and its result will be available in the next cycle.
Meanwhile, the first FMUL is sent to the ROB and the first available RS where it will wait for its operands (F1/ROB0)
Inst. Queue.
Reorder Buffer
Registers
Load Buffer
Reservation Station (FP)
Reservation Station (Int)
Common Data Bus
FMUL | ROB0 | 10 | ROB1
fsw f2, -4(t0)
fmul.s f2, f1, f0
flw f1, -4(t0)
bnez t0, loop
addi t0, t0, -4
fsw f2, -4(t0)
0 | FLW | F1 | 
1 | FMUL | F2 | 
2 |  |  | 
3 |  |  | 
4 |  |  | 
5 |  |  | 
F0 | 10 | 
F1 | 0 | ROB0
F2 | 0 | ROB1
T0 | 8 | 
FP ALU
Int ALU
Memory Unit
loads
inst.
commit
Op.+ROB#
operands
results
stores
fmul.s f2, f1, f0
fmul.s f2, f1, f0
flw f1, -4(t0)

## Slide 5
Cycle 3
The result of the first load is sent from the MU to the CDB, where it will be copied to the ROB and the RS waiting for it.
Inst. Queue.
Reorder Buffer
Registers
Load Buffer
Reservation Station (FP)
Reservation Station (Int)
Common Data Bus
FMUL | 1 | 10 | ROB1
fsw f2, -4(t0)
fmul.s f2, f1, f0
flw f1, -4(t0)
bnez t0, loop
addi t0, t0, -4
fsw f2, -4(t0)
0 | FLW | F1 | 1
1 | FMUL | F2 | 
2 |  |  | 
3 |  |  | 
4 |  |  | 
5 |  |  | 
F0 | 10 | 
F1 | 0 | ROB0
F2 | 0 | ROB1
T0 | 8 | 
FP ALU
Int ALU
Memory Unit
loads
inst.
commit
Op.+ROB#
operands
results
stores
flw f1, -4(t0)

## Slide 6
Cycle 3
Still in cycle 3, the first store op is sent to the ROB where it will wait for F2/ROB1. This way, the ROB acts as a store buffer.
Inst. Queue.
Reorder Buffer
Registers
Load Buffer
Reservation Station (FP)
Reservation Station (Int)
Common Data Bus
FMUL | 1 | 10 | ROB1
addi t0, t0, -4
fsw f2, -4(t0)
fmul.s f2, f1, f0
flw f1, -4(t0)
bnez t0, loop
addi t0, t0, -4
0 | FLW | F1 | 1
1 | FMUL | F2 | 
2 | FSW | Mem[4] | F2/ROB1
3 |  |  | 
4 |  |  | 
5 |  |  | 
F0 | 10 | 
F1 | 0 | ROB0
F2 | 0 | ROB1
T0 | 8 | 
FP ALU
Int ALU
Memory Unit
loads
inst.
commit
Op.+ROB#
operands
results
stores
fsw f2, -4(t0)

## Slide 7
Cycle 4
The first load (FLW) commits to the register file (F1).
Meanwhile the first FMUL is sent to the FP ALU because it now has all operands.
The first ADDI is sent to the RS and the ROB.
Inst. Queue.
Reorder Buffer
Registers
Load Buffer
Reservation Station (FP)
Reservation Station (Int)
Common Data Bus
bnez t0, loop
addi t0, t0, -4
fsw f2, -4(t0)
fmul.s f2, f1, f0
flw f1, -4(t0)
bnez t0, loop
1 | FMUL | F2 | 
2 | FSW | Mem[4] | F2/ROB1
3 | ADDI | T0 | 
4 |  |  | 
5 |  |  | 
0 |  |  | 
F0 | 10 | 
F1 | 1 | 
F2 | 0 | ROB1
T0 | 8 | ROB3
ADDI | 8 | -4 | ROB3
FP ALU
Int ALU
Memory Unit
loads
inst.
commit
Op.+ROB#
operands
results
stores
addi t0, t0, -4
fmul.s f2, f1, f0
addi t0, t0, -4​

## Slide 8
Cycle 5
The branch (BNEZ) is sent to the ROB and the RS where it will wait for its operands (T0/ROB3).
The ADDI instruction is sent to the Int ALU because it has all operands.
Inst. Queue.
Reorder Buffer
Registers
Load Buffer
Reservation Station (FP)
Reservation Station (Int)
Common Data Bus
flw f1, -4(t0)
bnez t0, loop
addi t0, t0, -4
fsw f2, -4(t0)
fmul.s f2, f1, f0
flw f1, -4(t0)
1 | FMUL | F2 | 
2 | FSW | Mem[4] | F2/ROB1
3 | ADDI | T0 | 
4 | BNEZ | ? | 
5 |  |  | 
0 |  |  | 
F0 | 10 | 
F1 | 1 | 
F2 | 0 | ROB1
T0 | 8 | ROB3
BNEZ | ROB3 | - | ROB4
FP ALU
Int ALU
Memory Unit
loads
inst.
commit
Op.+ROB#
operands
results
stores
bnez t0, loop
bnez t0, loop
addi t0, t0, -4

## Slide 9
Cycle 6
The second load (FLW) is sent to the ROB and the Load Buffer where it will wait for ROB3/T0.
The result of the ADDI instruction is broadcast through the CDB to the ROB and RS waiting for it.
Inst. Queue.
Reorder Buffer
Registers
Load Buffer
Reservation Station (FP)
Reservation Station (Int)
Common Data Bus
ROB3 | ROB5
fmul.s f2, f1, f0
flw f1, -4(t0)
bnez t0, loop
addi t0, t0, -4
fsw f2, -4(t0)
fmul.s f2, f1, f0
1 | FMUL | F2 | 
2 | FSW | Mem[4] | F2/ROB1
3 | ADDI | T0 | 4
4 | BNEZ | ? | 
5 | FLW | F1 | 
0 |  |  | 
F0 | 10 | 
F1 | 1 | ROB5
F2 | 0 | ROB1
T0 | 8 | ROB3
BNEZ | 4 | - | ROB4
FP ALU
Int ALU
Memory Unit
loads
inst.
commit
Op.+ROB#
operands
results
stores
flw f1, -4(t0)
flw f1, -4(t0)
addi t0, t0, -4

## Slide 10
Cycle 7
The load FLW/ROB5 gets operand ROB3/T0 from the ROB.
The 2nd FMUL is sent to the RS and the ROB.
Note how registers file for F2 now points to ROB0.
Inst. Queue.
Reorder Buffer
Registers
Load Buffer
Reservation Station (FP)
Reservation Station (Int)
Common Data Bus
0 | ROB5
FMUL | ROB5 | 10 | ROB0
fsw f2, -4(t0)
fmul.s f2, f1, f0
flw f1, -4(t0)
bnez t0, loop
addi t0, t0, -4
fsw f2, -4(t0)
1 | FMUL | F2 | 
2 | FSW | Mem[4] | F2/ROB1
3 | ADDI | T0 | 4
4 | BNEZ | ? | 
5 | FLW | F1 | 
0 | FMUL | F2 | 
F0 | 10 | 
F1 | 1 | ROB5
F2 | 0 | ROB0
T0 | 8 | ROB3
BNEZ | 4 | - | ROB4
FP ALU
Int ALU
Memory Unit
loads
inst.
commit
Op.+ROB#
operands
results
stores
fmul.s f2, f1, f0
fmul.s f2, f1, f0

## Slide 11
Cycle 7
Still in cycle 7, the ROB gets the result of the first FMUL operation (10). The first FSW (store) was waiting for it.
The BNEZ instruction is sent to the ALU.
Inst. Queue.
Reorder Buffer
Registers
Load Buffer
Reservation Station (FP)
Reservation Station (Int)
Common Data Bus
0 | ROB5
FMUL | ROB5 | 10 | ROB0
fsw f2, -4(t0)
fmul.s f2, f1, f0
flw f1, -4(t0)
bnez t0, loop
addi t0, t0, -4
fsw f2, -4(t0)
1 | FMUL | F2 | 10
2 | FSW | Mem[4] | 10
3 | ADDI | T0 | 4
4 | BNEZ | ? | 
5 | FLW | F1 | 
0 | FMUL | F2 | 
F0 | 10 | 
F1 | 1 | ROB5
F2 | 0 | ROB0
T0 | 8 | ROB3
FP ALU
Int ALU
Memory Unit
loads
inst.
commit
Op.+ROB#
operands
results
stores
fmul.s f2, f1, f0
bnez t0, loop

## Slide 12
Cycle 8
The second FSW can't enter the pipeline because the ROB is full.
The 2nd load is sent to the MU.
The first 3 instructions of the ROB commit to the register file AND memory (FSW).
The first BNEZ gets its result: prediction correct. No need to flush the ROB.
Inst. Queue.
Reorder Buffer
Registers
Load Buffer
Reservation Station (FP)
Reservation Station (Int)
Common Data Bus
FMUL | ROB5 | 10 | ROB0
fsw f2, -4(t0)
fmul.s f2, f1, f0
flw f1, -4(t0)
bnez t0, loop
addi t0, t0, -4
fsw f2, -4(t0)
4 | BNEZ | CORRECT | 
5 | FLW | F1 | 
0 | FMUL | F2 | 
1 |  |  | 
2 |  |  | 
3 |  |  | 
F0 | 10 | 
F1 | 1 | ROB5
F2 | 10 | ROB0
T0 | 4 | 
FP ALU
Int ALU
Memory Unit
loads
inst.
commit
Op.+ROB#
operands
results
stores
bnez t0, loop
flw f1, -4(t0)

## Slide 13
Cycle 9
We get the result of the second load, FLW (2). Both the ROB and the RS waiting for it.
Since the first BNEZ branch prediction was correct, we clear it silently from the ROB.
The second store, FSW, enters the ROB.
Inst. Queue.
Reorder Buffer
Registers
Load Buffer
Reservation Station (FP)
Reservation Station (Int)
Common Data Bus
FMUL | 2 | 10 | ROB0
addi t0, t0, -4
fsw f2, -4(t0)
fmul.s f2, f1, f0
flw f1, -4(t0)
bnez t0, loop
addi t0, t0, -4
5 | FLW | F1 | 2
0 | FMUL | F2 | 
1 | FSW | Mem[0] | F2/ROB0
2 |  |  | 
3 |  |  | 
4 |  |  | 
F0 | 10 | 
F1 | 1 | ROB5
F2 | 10 | ROB0
T0 | 4 | 
FP ALU
Int ALU
Memory Unit
loads
inst.
commit
Op.+ROB#
operands
results
stores
fsw f2, -4(t0)
flw f1, -4(t0)

## Slide 14
Cycle 10
The second ADDI enters the ROB and the RS.
The second load (FLW) commits. Its value is written to the registers (2).
The second FMUL goes to the FP ALU because it now has all operands.
Inst. Queue.
Reorder Buffer
Registers
Load Buffer
Reservation Station (FP)
Reservation Station (Int)
Common Data Bus
bnez t0, loop
addi t0, t0, -4
fsw f2, -4(t0)
fmul.s f2, f1, f0
flw f1, -4(t0)
bnez t0, loop
0 | FMUL | F2 | 
1 | FSW | Mem[0] | F2/ROB0
2 | ADDI | T0 | 
3 |  |  | 
4 |  |  | 
5 |  |  | 
F0 | 10 | 
F1 | 2 | 
F2 | 10 | ROB0
T0 | 4 | ROB2
ADDI | 4 | -4 | ROB2
FP ALU
Int ALU
Memory Unit
loads
inst.
commit
Op.+ROB#
operands
results
stores
addi t0, t0, -4
addi t0, t0, -4
fmul.s f2, f1, f0

## Slide 15
Cycle 11
The second ADDI is sent to the ALU.
The second BNEZ enters the ROB and RS.
Inst. Queue.
Reorder Buffer
Registers
Load Buffer
Reservation Station (FP)
Reservation Station (Int)
Common Data Bus
flw f1, -4(t0)
bnez t0, loop
addi t0, t0, -4
fsw f2, -4(t0)
fmul.s f2, f1, f0
flw f1, -4(t0)
0 | FMUL | F2 | 
1 | FSW | Mem[0] | F2/ROB0
2 | ADDI | T0 | 
3 | BNEZ | ? | 
4 |  |  | 
5 |  |  | 
F0 | 10 | 
F1 | 2 | 
F2 | 10 | ROB0
T0 | 4 | ROB2
BNEZ | ROB2 | - | ROB3
FP ALU
Int ALU
Memory Unit
loads
inst.
commit
Op.+ROB#
operands
results
stores
bnez t0, loop
bnez t0, loop
addi t0, t0, -4

## Slide 16
Cycle 12
The result of the second ADDI is sent through the CDB to the ROB and the RS waiting for it.
The third load, FLW, enters the ROB and the LB where it will wait for T0/ROB2.
Inst. Queue.
Reorder Buffer
Registers
Load Buffer
Reservation Station (FP)
Reservation Station (Int)
Common Data Bus
ROB2 | ROB4
fmul.s f2, f1, f0
flw f1, -4(t0)
bnez t0, loop
addi t0, t0, -4
fsw f2, -4(t0)
fmul.s f2, f1, f0
0 | FMUL | F2 | 
1 | FSW | Mem[0] | F2/ROB0
2 | ADDI | T0 | 0
3 | BNEZ | ? | 
4 | FLW | F1 | 
5 |  |  | 
F0 | 10 | 
F1 | 2 | ROB4
F2 | 10 | ROB0
T0 | 4 | ROB2
BNEZ | 0 | - | ROB3
FP ALU
Int ALU
Memory Unit
loads
inst.
commit
Op.+ROB#
operands
results
stores
flw f1, -4(t0)
flw f1, -4(t0)
addi t0, t0, -4

## Slide 17
Cycle 13
The result of the second FMUL is sent through the CDB to the ROB and RS.
The third load (FLW) gets its operand T0/ROB2 from the ROB.
The BNEZ is sent to the ALU since it now has all its operands.
Inst. Queue.
Reorder Buffer
Registers
Load Buffer
Reservation Station (FP)
Reservation Station (Int)
Common Data Bus
-4 | ROB4
FMUL | ROB4 | 2 | ROB5
fsw f2, -4(t0)
fmul.s f2, f1, f0
flw f1, -4(t0)
bnez t0, loop
addi t0, t0, -4
fsw f2, -4(t0)
0 | FMUL | F2 | 20
1 | FSW | Mem[0] | 20
2 | ADDI | T0 | 0
3 | BNEZ | ? | 
4 | FLW | F1 | 
5 | FMUL | F2 | 
F0 | 10 | 
F1 | 2 | ROB4
F2 | 10 | ROB5
T0 | 4 | ROB2
FP ALU
Int ALU
Memory Unit
loads
inst.
commit
Op.+ROB#
operands
results
stores
fmul.s f2, f1, f0
fmul.s f2, f1, f0
fmul.s f2, f1, f0
bnez t0, loop

## Slide 18
Cycle 14
FSW doesn't enter the pipeline because there is no space in the ROB.
The first 3 entries in the ROB commit to the Register File and memory.
The third load is sent to the MU.
We get the results of the BNEZ instruction from the ALU: prediction incorrect.
Inst. Queue.
Reorder Buffer
Registers
Load Buffer
Reservation Station (FP)
Reservation Station (Int)
Common Data Bus
FMUL | ROB4 | 2 | ROB5
fsw f2, -4(t0)
fmul.s f2, f1, f0
flw f1, -4(t0)
bnez t0, loop
addi t0, t0, -4
fsw f2, -4(t0)
3 | BNEZ | INCORRE | 
4 | FLW | F1 | 
5 | FMUL | F2 | 
0 |  |  | 
1 |  |  | 
2 |  |  | 
F0 | 10 | 
F1 | 2 | ROB4
F2 | 20 | ROB5
T0 | 0 | 
FP ALU
Int ALU
Memory Unit
loads
inst.
commit
Op.+ROB#
operands
results
stores
bnez t0, loop
flw f1, -4(t0)

## Slide 19
Cycle 15
The third BNEZ hits the ROB head and the branch prediction was incorrect. We need to clear all instructions after the BNEZ from the pipeline and resume the execution at the correct point.
Inst. Queue.
Reorder Buffer
Registers
Load Buffer
Reservation Station (FP)
Reservation Station (Int)
Common Data Bus
FMUL | ROB4 | 2 | ROB5
fsw f2, -4(t0)
fmul.s f2, f1, f0
flw f1, -4(t0)
bnez t0, loop
addi t0, t0, -4
fsw f2, -4(t0)
3 | BNEZ | INCORRE | 
4 | FLW | F1 | 
5 | FMUL | F2 | 
0 |  |  | 
1 |  |  | 
2 |  |  | 
F0 | 10 | 
F1 | 2 | ROB4
F2 | 20 | ROB5
T0 | 0 | 
FP ALU
Int ALU
Memory Unit
loads
inst.
commit
Op.+ROB#
operands
results
stores

## Slide 20
Cycle 16
We resume the execution at the correct point.
Inst. Queue.
Reorder Buffer
Registers
Load Buffer
Reservation Station (FP)
Reservation Station (Int)
Common Data Bus
fadd.s f1,f5,f2
fdiv.s f0,f3,f1
fsub.s f5,f1,f2
fmul.s f3,f2,f4
4 |  |  | 
5 |  |  | 
0 |  |  | 
1 |  |  | 
2 |  |  | 
3 |  |  | 
F0 | 10 | 
F1 | 2 | 
F2 | 20 | 
T0 | 0 | 
FP ALU
Int ALU
Memory Unit
loads
inst.
commit
Op.+ROB#
operands
results
stores